## Slide 1: The ERP Boot Camp
What Are ERPs and What Are They Good For?

## Slide 2: Overview
A bit of history: The first cognitive ERP study
Review: Basic electricity & neurophysiology
Neural origins of ERPs
What are ERPs good for?
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 3: The First Cognitive ERP Study
Walter, W. G., Cooper, R., Aldridge, V. J., McCallum, W. C., & Winter, A. L. (1964). Contingent negative variation: An electric sign of sensorimotor association and expectancy in the human brain. Nature, 203, 380-384.
1964: Gray Walter and the CNV
No Task: Click Only
No Task: Flashes Only
No Task: Click followed by flashes
Task: Press button when flashes start
CNV
Notes: Figure 1 from Walter, W. G., Cooper, R., Aldridge, V. J., McCallum, W. C., & Winter, A. L. (1964). Contingent negative variation: An electric sign of sensorimotor association and expectancy in the human brain. Nature, 203, 380-384. Reprinted by permission from Macmillan Publishers Ltd: NATURE (203) copyright (1964). This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.
Other content: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 4: Which Way is Up?
Walter, W. G., Cooper, R., Aldridge, V. J., McCallum, W. C., & Winter, A. L. (1964). Contingent negative variation: An electric sign of sensorimotor association and expectancy in the human brain. Nature, 203, 380-384.
Notes: Figure 1 from Walter, W. G., Cooper, R., Aldridge, V. J., McCallum, W. C., & Winter, A. L. (1964). Contingent negative variation: An electric sign of sensorimotor association and expectancy in the human brain. Nature, 203, 380-384. Reprinted by permission from Macmillan Publishers Ltd: NATURE (203) copyright (1964). This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 5: Which Way is Up?
René Descartes
Notes: Public domain painting of Descartes from wikipedia
Public domain example of Cartesian coordinate system from wikipedia
Other content: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 6: The Oddball Paradigm
= Standard
= Deviant/Oddball/Target
Typical Task Alternatives:
Count oddballs
Press only for oddballs
Different buttons for standard, oddball
P2
N2
P3
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 7: Some Terminology
Duration
Interstimulus Interval
(ISI)
Stimulus Onset Asynchrony
(SOA)
Intertrial Interval
(ITI)
SOA
ISI
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 8: Some Basics of Neuroscience
Resting membrane potential
  -70 mV on inside of cell
Action potentials
  Triggered when membrane potential goes sufficiently positive
  Starts at axon hillock and travels down axon
  Rarely contributes to scalp ERPs
Postsynaptic potentials (PSPs)
  Neurotransmitter binds with receptor, opens ion channels
  Excitatory: Positive charges move into cell
  Inhibitory: Negative charges move into cell
  The origin of most ERPs
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 9: Some Basics of Electricity
AC is “Alternating Current”
  Changes fairly rapidly over time
  Line current (50 or 60 Hz)
  EEG
DC is “Direct Current”
  Fairly constant “offset” in voltage
  Batteries
  Skin potentials
  In discussions of amplifiers, DC can also mean “Direct Coupled” (as opposed to capacitively coupled)
    Conveniently, this means that a DC (direct coupled) amplifier can amplify DC (direct current) signals
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 10: Some Basics of Electricity
Current (I for Intensity; Amperes)
  Movement of charges across space (coulombs per second)
  Like rate of water coming out of a hose (liters per second)
Voltage (E for Electromotive Force; Volts)
  Potential for charges to move
  Like water pressure
Resistance (R; Ohms [Ω])
  Resistance to movement of charges
  Like having a skinny or blocked hose segment
Impedance (Z)
  Resistance to the flow of alternating current (AC)
  Combines resistance, capacitance, and inductance
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 11: Some Basics of Electricity
Power (Watts) = EI (typically proportional to E2)
  Power = Amplitude2
  Amplitude = sqrt(Power)
Ohm’s Law: E = IR
  If resistance increases and current is constant, voltage increases!
  If you keep total water flow constant but constrict part of the hose, the pressure increases
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 12: Some Basics of Electricity
Induction
  If you pass an electrical current through a conductor, a magnetic field will run around it (right-hand rule)
  If you pass a magnetic field across a conductor, an electrical current is induced in the conductor
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 13: Where Do ERPs Come From?
Cortical pyramidal cell (basic input-output cell of cerebral cortex)
Excitatory transmitter released on apical dendrites causes positive charges to flow into dendrites
Net negative on outside of cell
Current flows through cell, completing the circuit
Polarity reverses with inhibitory transmitter
Polarity reverses with PSP on cell body and basal dendrites
Polarity at scalp also depends on orientation of the cortical surface and position of reference electrode
For a recent review, see Buzsáki, Anastassiou, & Koch (2012, Nature Reviews Neuroscience)
Notes: Portion of Figure 5.2 reprinted from Luck, S. J., & Girelli, M. (1998). Electrophysiological approaches to the study of selective attention in the human brain. In R. Parasuraman (Ed.), The Attentive Brain (pp. 71-94). Cambridge, MA: MIT Press. © MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.
Other content: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 14: Where Do ERPs Come From?
To be recorded at a distance, large numbers of neurons must have similar voltage fields
Equivalent Current Dipole
Notes: Portion of Figure 5.2 reprinted from Luck, S. J., & Girelli, M. (1998). Electrophysiological approaches to the study of selective attention in the human brain. In R. Parasuraman (Ed.), The Attentive Brain (pp. 71-94). Cambridge, MA: MIT Press. © MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.
Other content: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 15: Where Do ERPs Come From?
Scalp-recorded potentials are possible only for layered structures with consistent orientations
Primarily cerebral cortex
What about:
Brainstem nuclei?
Superior colliculus?
Possible role of radial glia
Local Field Potentials
Open Field
Closed Field
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 16: Where Do ERPs Come From?
Voltages spread through the brain by “volume conduction”
Nearly speed of light
Voltage everywhere except at positive-negative transition
Skull causes lateral spread (like spraying hose on cardboard)
Notes: Portion of Figure 5.2 reprinted from Luck, S. J., & Girelli, M. (1998). Electrophysiological approaches to the study of selective attention in the human brain. In R. Parasuraman (Ed.), The Attentive Brain (pp. 71-94). Cambridge, MA: MIT Press. © MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.
© S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 17: Magnetoencephalography (MEG)
Example:
Mismatch
Negativity
Woldorff et al (1993)
Magnetic Field
Voltage Distribution
Efflux
Influx
–
+
The skull is transparent to magnetism -- less blurring
Deep and radial dipoles are invisible from outside the head
Notes: Portion of Figure 5.2 from Luck, S. J., & Girelli, M. (1998). Electrophysiological approaches to the study of selective attention in the human brain. In R. Parasuraman (Ed.), The Attentive Brain (pp. 71-94). Cambridge, MA: MIT Press.
Photo from http://www.4dneuroimaging.com/Magnes%20Product%20Line.html
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 18: The Superposition Problem
w1,1
w2,1
w3,1
w1,2
w2,2
w3,2
w1,3
w2,3
w3,3
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
C1
C2
C3
E1
C1
C2
C3
E2
E1
E3
Voltage at an electrode at time t is a weighted sum of all components that are active at time t
There is no foolproof way to recover the underlying components from the observed waveforms
E2
E3
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 19
Initial Sensory Response
Stimulus Onset
Higher Perceptual Processes
Task-Dependent Categorization
Response Selection
Working Memory Encoding
Post-Response Evaluation
Prestimulus Preparatory Processes
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 20
Clap once if you see a person in the following photograph
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 21
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 22
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 23
Notes: https://commons.wikimedia.org/wiki/File:US_Navy_060607-N-2832L-053_Air_Force_Col._Jeffrey_Swartz,_a_dentist,_pulls_teeth_from_patients_aboard_the_U.S._Military_Sealift_Command_(MSC)_hospital_ship_USNS_Mercy_(T-AH_19).jpg
Public Domain

## Slide 24
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 25
An Example:
Visual Working Memory
Notes: http://www.flickr.com/photos/myheimu/7995211914
Creative Commons 2.0

## Slide 26
Notes: Annoying my sister – one of the many services I offer

## Slide 27
An Example:
Visual Working Memory
Notes: https://commons.wikimedia.org/wiki/File:Baby_on_Back.jpg
Creative Commons 3.0

## Slide 28
Notes: Annoying my sister – one of the many services I offer

## Slide 29: Temporal Resolution
Gist of a scene available within 150-250 ms
Eye movements every 200-500 ms
  Low-level sensory processing
  Focus attention on relevant information
  Identify it
  Store it in working memory
  Find next saccade target
  Program and execute eye movement
ERPs allow us to measure these individual processes as they are happening
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 30: Temporal Resolution
In behavioral button-press tasks, all this stuff is combined into a single output
In fMRI, all is collapsed into a single time slice
ERPs:
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 31: What are ERPs Good For?
Stimulus
Response
All the good stuff
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 32: What are ERPs Good For?
Determine whether an experimental manipulation influenced Process A or Process B
  What was the onset time of the difference?
  Which ERP component was affected by the manipulation?
Identifying multiple neurocognitive processes
  A given behavioral effect is often accompanied by multiple ERP effects (different components)
  Easy to identify multiple processes contributing to behavior
Covert monitoring of processing
  Processing can be measured without a behavioral response (or from subjects who cannot easily respond)
  Did the brain do something that was not evident in behavior?
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 33: What are ERPs Good For?
Link to the brain
  Under some conditions, neural systems can be identified
  But people often draw unwarranted conclusions about underlying neural processes from ERPs
  Many researchers desperately want ERPs to be like fMRI or single-unit recordings, but they are not
  “Those English boys want to play the blues so bad—and they DO play it so bad” — Sonny Boy Williamson
  “Those ERPers want to study the brain so bad—and they DO study it so bad” — Sonny Boy Luck
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 34: ERPs as Biomarkers
ERPs are tightly tied to neurotransmission
  MMN may reflect current flow through NMDA receptors
  A change in ERPs reflects a change in PSPs (not mediated through hemodynamic response)
Rodent/primate models available for some components
  Potentially useful as an assay in drug discovery
Easily tolerated by patients
Some paradigms have excellent stability, reliability
Relatively inexpensive, feasible for large-N studies
May be able to predict which patients will respond to a given treatment
Potential roadblocks
  Individual differences, lack of quality assurance standards
See Luck et al. (2011, Biological Psychiatry)
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 35: ERPs May be Bad When…
You desire certainty about the neuroanatomical locus of an effect
You are interested in activity that is slow (>~2 s) or not time-locked to a sudden, observable event
You cannot collect large numbers of trials in each critical condition
  Long period of time between trials
  Severe adaptation of response over trials
  Need to surprise subjects
The process of interest does not have an ERP signature
Subjects make frequent head, eye, or mouth movements during the time period of interest
  Speech is particularly bad (tongue has strong dipole)
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 36: Drift Over Time
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 37: Comparison of Techniques
Also…
  If you want to study the sequence of processes from 0-1000 ms, use ERPs; if you want to differentiate V2 from V4, use fMRI
  Tolerability: Infants and children, obese people, anxious people
  ERPs best for transient activity; fMRI best for sustained activity
  Brain areas more intrinsically meaningful than ERP components
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.