## Slide 1: The ERP Boot Camp
Artifact Detection and Rejection

## Slide 2: Ocular Artifacts
Lins, Picton, Berg, & Scherg (1993)
Noncephalic reference
Notes: Figure 3 and Figure 4 Lins, Picton, Berg, Scherg (1993) Ocular artifacts in recording EEGs and event-related potentials. I: Scalp Topography. Brain Topography 6,1. 51-63. Reprinted with permission from Springer. © Springer. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 3: Artifact Rejection: Why?
Reason 1: Noise reduction
  Artifacts are a large noise signal
Reason 2: Control sensory input
  Subject may not have eyes open or directed at stimuli
Reason 3: Systematic distortion of data
  If subjects blink more for some kinds of stimuli than others, this will create a large artifact in the averaged ERPs
  Same for vertical eye movements
  Horizontal eye movements can distort N2pc and LRP
Artifact correction can deal with #1 and #3 but not #2
  We will discuss artifact correction later
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 4: Artifact Rejection: How?
Goal: Throw out trials with problematic artifacts; don’t throw out “good” trials
  Throw out all channels if an artifact is detected in any channel
Problem: There is a continuum of “goodness”
Signal detection problem
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 5: Artifact Rejection: How?
Goal: Throw out trials with problematic artifacts; don’t throw out “good” trials
  Throw out all channels if an artifact is detected in any channel
Problem: There is a continuum of “goodness”
Signal detection problem
  We have a measure of strength of artifact
    Tends to be bigger when artifact is actually present
    A good measure is big for present, small for absent
  We set a rejection threshold
  Any trials that exceed this threshold are thrown away
  Best threshold depends on relative costs of misses and false alarms
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 6: Changing the Threshold
Rejected
Not Rejected – False Negative
Not Rejected
Not Rejected
Rejected
Rejected
Not Rejected
Rejected – False Positive
To optimize artifact rejection, we need a measure that is tailored for the kind of artifact we are trying to reject; this requires knowing something about the artifacts
Notes: Adapted from Figure 6.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 7: Blink Shape and Propagation
Active: Under Eye
Reference: Rm
Common to use VEOG-lower minus VEOG-upper
Notes: Figure 4.8 from Luck, Steven J. (2005). An introduction to the Event-Related Potential Technique. Cambridge, MA: MIT Press.© MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 8: Absolute Threshold and Baseline Correction
Before Baseline Correction
After Baseline Correction
Notes: Adapted from Figure 6.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 9: Peak-to-Peak Amplitude
Peak-to-peak amplitude:
Difference between most positive and most negative voltage in the rejection window
Notes: Adapted from Figure 6.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 10: Moving Window Peak-to-Peak
Moving window
peak-to-peak amplitude:
Find biggest peak-to-peak amplitude in several small, overlapping windows
Takes advantage of the fact that a blink occurs over a period of about 200 ms
Notes: Adapted from Figure 6.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 11: Minimizing Blinks
No contact lenses
Frequent breaks
Times when blinks are OK
  But be careful of blink offsets
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 12: Assessing Success
Was blink rejection successful?
  Look for polarity inversions
  Baseline impacted by blinks in this example
  Experimental effect not due to blinks
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 13: Saccadic Eye Movements
Eyes contain dipole with positive end pointing toward front of eye
Amplitude linearly related to size of eye movement (16 µV/degree)
Active: HEOG-L
Reference: HEOG-R
Step Function: Find largest difference in mean voltage between consecutive 100-ms time intervals
Notes: Adapted from Figure 4.9 inLuck, Steven J. (2005). An introduction to the Event-Related Potential Technique. Cambridge, MA: MIT Press.© MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 14: Fixation Point
Best fixation point
  Empirically demonstrated to minimize dispersion and microsaccades
  Thaler, Lore, Schütz, Alexander C, Goodale, Melvyn A, & Gegenfurtner, Karl R. (2013). What is the best fixation target? The effect of target shape on stability of fixational eye movements. Vision Research, 76, 31-42.
Usually best for the fixation point to be continuously visible
  Otherwise you get an onset response to the fixation point
  But brief disappearance of fixation point can be a good way to signal the time period in which blinks are allowed
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 15: Minimizing and Detecting Saccades
Design experiment so that subjects don’t have any reason to deviate from fixation
If this is not possible, use two-tiered strategy
  Use step function to throw out trials with large eye movements
  Compute averaged HEOG waveforms for L and R targets
  Throw out subjects with residual HEOG > some threshold
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 16: Step Function & Blinks
Step Function:
Find largest difference in mean voltage between consecutive 100-ms time intervals
Takes advantage of the fact that a blink consists of a period of one voltage followed by a period of a much larger voltage
Notes: Adapted from Figure 6.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 17: Setting Rejection Parameters
Need to select threshold, electrode sites, overall rejection window, moving window length
Recommended strategy (subject-specific)
  Artifacts differ in type, size, and timing across subjects
  Start with parameters based on previous experience
  Look at single trials to assess false positives & negatives
  Adjust parameters to achieve optimal balance between removing problematic artifacts and maintaining # of trials
  Check percentage of rejected trials
  Iterate until satisfied
To avoid bias in within-subject designs
  Do not do not base parameters on condition-specific ERPs
To avoid bias in between-subject designs
  Have rejection done by someone who is blind to group
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 18: Commonly Recorded Artifactual Potentials (C.R.A.P.)
(Don’t try to reject: Minimize and/or Correct)
EMG
Temporalis muscles, forehead muscles, neck muscles
Just ask subjects to relax and sit in a neutral position
Notes: Adapted from Figure 4.9 in Luck, Steven J. (2005). An introduction to the Event-Related Potential Technique. Cambridge, MA: MIT Press.© MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 19: Commonly Recorded Artifactual Potentials (C.R.A.P.)
(Don’t try to reject: Minimize and/or Correct)
EKG
Conducted via carotid arteries
Usually picked up by mastoid reference electrodes
Don’t try to eliminate…
Notes: Adapted from Figure 4.9 in Luck, Steven J. (2005). An introduction to the Event-Related Potential Technique. Cambridge, MA: MIT Press.© MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 20: Commonly Recorded Artifactual Potentials (C.R.A.P.)
(Don’t try to reject: Minimize and/or Correct)
Blocking
Should occur only if your ADC is 12-16 bits
Reduce amplifier gain
Notes: Adapted from Figure 4.9 in Luck, Steven J. (2005). An introduction to the Event-Related Potential Technique. Cambridge, MA: MIT Press.© MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 21: Commonly Recorded Artifactual Potentials (C.R.A.P.)
(Don’t try to reject: Minimize and/or Correct)
Skin potentials
Constant cool temperature
Low electrode impedance
High-pass filter at 0.1 Hz
Notes: Adapted from Figure 4.9 in Luck, Steven J. (2005). An introduction to the Event-Related Potential Technique. Cambridge, MA: MIT Press.© MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 22: Commonly Recorded Artifactual Potentials (C.R.A.P.)
(Don’t try to reject: Minimize and/or Correct)
Alpha
Largest over posterior scalp sites
Often suppressed by stimulus onset
Minimize with breaks, interesting tasks, caffeine
Is caffeine a confound? Should you report it?
Notes: Adapted from Figure 4.9 in Luck, Steven J. (2005). An introduction to the Event-Related Potential Technique. Cambridge, MA: MIT Press.© MIT Press. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.