## Slide 1: The ERP Boot Camp
Statistical Analysis of ERP Data

## Slide 2: Lecture Overview
Review of basic stats terminology
Truth vs. statistical significance
The world’s best statistic
The standard approach to ERP analysis
The million dollar statistical approach
  How to go from p = .258 to p = .0017 (ethically)
The problem of multiple comparisons in ERP research
  How flexibility in choosing time windows and electrode sites leads to bogus findings
  Appropriate methods for choosing time windows and electrodes sites
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 3: Some Terminology
Null hypothesis vs. alternative hypothesis
Type I error
  False positive: Rejecting the null hypothesis when it is true
  “Bogus effect”
Type II error
  False negative: Accepting the null hypothesis when it is false
Alpha
  Nominal probability that a Type I error rate will occur
  Usually .05
Statistical power
  Probability that a real effect will be significant in a given effect
  Depends on size of effect, amount of error variance, number of subjects
Experimentwise/Familywise error rate
  Probability that at least one p value from a set of related analyses will be significant even if the null hypothesis is true for all effects
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 4: Some Terminology
Example: Oddball experiment
  Separate ANOVAs for P3 amplitude and P3 latency
  3 Factors: Group, Target/Standard, Electrode Site
  Each ANOVA has 7 p values: 3 main effects, 3 two-way interactions, 1 three-way interaction
  14 total p values (7 for amplitude + 7 for latency)
If null is true for all 14 effects, what is the probability that at least one p-value is < .05?
  Approximately 50%!!!
All else being equal, you should try to reduce the number of ANOVAs per experiment and the number of factors per ANOVA
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 5: The World’s Best Statistic
Replication is the best statistic
  The .05 threshold is arbitrary
    What would happen if we decided the threshold should be .06?
  We regularly violate the assumptions of statistical tests, so the computed p-values are not correct estimates of probability of a Type I error
  The real question is whether the effects are real or noise
  If they are real (and large enough), they will be replicable
General advice
  Collect clean data with big effects
  Use a simple and straightforward statistical approach
  Run follow-up experiments that contain replications
  or
  Find a really good statistician who can do the most appropriate statistical tests
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 6: Context of Discovery vs. Context of Justification
New discoveries often come from looking at data, not from testing a priori hypotheses
  Example: Discovery of N2pc, CDA, ERN, N400
Early in the research process, you need to look at your data in a million different ways, computing hundreds or thousands of p values with no correction for multiple comparisons
  You can advance your career in the short run by publishing the significant results as if they were predicted by a cool theory
  But long-term success arises when other people build on your results, which won’t happen if they are bogus
Once you believe you’ve found something, run follow-up experiments to demonstrate (to yourself and the world) that your findings are reliable
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 7: Standard Approach
First, collapse across irrelevant factors
  If target and standard are counterbalanced, collapse to avoid physical stimulus differences
  This reduces number of ANOVA factors
    Fewer p values
    Fewer spurious interactions
    Smaller experimentwise error
Measure amplitude and/or latency from each subject in each remaining condition
Do separate ANOVAs for amplitude and latency of each key component
  When possible, have a single ANOVA as your primary analysis to reduce experimentwise error
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 8: Standard Approach
Use electrodes at which component is present
  Otherwise your effect may get swamped by noise at other electrodes
  Interaction with electrode site has low power
Electrode site is usually two factors
  Anterior-posterior and Left-middle-right
  But this increases # of factors
Use clusters if you have lots of electrodes
  Averaging across electrodes may reduce measurement error
  Average waveforms across sites first, then measure amplitudes/latencies (for nonlinear measures, like peaks)
  May use a single cluster to minimize # of factors
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 9: Electrode Interactions
Amplitudes are multiplicative across electrodes
  Fz amplitude might go from 1.0 µV to 1.5 µV, and Pz amplitude might go from 2 µV to 3 µV
This produces a condition x electrode site interaction
  Even without a change in neural generators
Multiplicative
Additive
Chart: 
| Condition A | Condition B | Condition C
Fz | 1 | 1.5 | 2
Cz | 1.5 | 2.25 | 2.5
Pz | 2 | 3 | 3
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 10: Electrode Interactions
McCarthy & Wood (1985): Normalize the Data
  Divide by vector length
Chart: 
| Condition A | Condition B | Condition C
Fz | 1 | 1.5 | 2
Cz | 1.5 | 2.25 | 2.5
Pz | 2 | 3 | 3
Chart: 
| Condition A | Condition B | Condition C
Fz | 0.37139 | 0.37139 | 0.45584
Cz | 0.55709 | 0.55709 | 0.5698
Pz | 0.74278 | 0.74278 | 0.68376
Now the conditions have the same overall amplitude
  Main effects are eliminated; they are assessed prior to normalization
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 11: Electrode Interactions
Technical Problem: Urbach & Kutas (2002) demonstrated that normalization does not actually work under many realistic conditions
  Many of these problems disappear if you measure from difference waves
Conceptual problem: The conclusions that can be drawn from an electrode site interaction are extremely weak
  Could be same generators, but change in relative amplitudes
  Could be same generators, but a change in relative latencies
General advice: Don’t worry about electrode interactions
  You can’t draw very strong conclusions from them, so just report them
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 12: Heterogeneity of Covariance
Within-subjects ANOVA assumes homogeneity of variance and covariance
  Modest heterogeneity of variance not a big problem
  Heterogeneity of covariance inflates Type I error rate
What is homogeneity of covariance?
  3 or more levels of a within-subjects factor
  Each level must be equally correlated with the other levels
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 13: Heterogeneity of Covariance
Subject 1
Subject 2
Subject 3
Cond
A
Cond
B
Cond
C
Within-Subjects ANOVA assumes:
Covariance(A, B) =
Covariance(B, C) =
Covariance(A, C)
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 14: Heterogeneity of Covariance
Why is this a special problem for ERPs?
  Covariance is lower for more distant electrode pairs than for nearby electrode pairs
  Whenever 3 or more electrodes are used, heterogeneity of covariance is likely
SPR mandates that papers deal with this problem
Greenhouse-Geisser epsilon adjustment
  Degree of nonsphericity is computed
  An adjustment factor, epsilon, is computed
  New df computed by multiplying epsilon by original df
  New df used for computing p-values
Greehouse-Geisser epsilon is overly conservative
  Can use Huynh-Feldt epsilon instead
Everyone should use epsilon adjustment for all studies, not just ERP studies
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 15: Jackknife Approach
Miller, Patterson, & Ulrich (1998)
  Hard to measure onset latency (and other nonlinear parameters) from noisy single-subject waveforms
  Much easier to measure from grand average
Measure from grand average of N-1 subjects N times (once excluding each subject)
Variance will be artificially low but can be corrected
  Fcorrected = Funcorrected ÷ (N-1)2 [N per condition]
  Between, within, main effects, interactions
  Jackknife can also be used with Pearson r
So precise that you may need to use interpolation to measure latencies between sample points
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 16: Jackknife Approach
Subject 1
Subject 2
Subject 3
Grand w/o
Subject 1
Grand w/o
Subject 2
Grand w/o
Subject 3
50% fractional peak latency
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 17: Jackknife Approach
Conventional ANOVA on LRP onset latency
  F(1, 20) = 1.315, p = 0.258
Jackknife ANOVA on LRP onset latency
  F(1, 20) = 5221.625, Fc = 13.05, p = .0017
Limitations
  Doesn’t help with linear measures
  Easier to have equal Ns for between-subjects ANOVAs
  Is sometimes worse than conventional approach
  Testing a slightly different null hypothesis
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 18: Jackknife Approach
Conventional null hypothesis
  If you measure from every individual in the population, the average of these measures does not differ across conditions
Jackknife null hypothesis
  If you make grand averages across every individual in the population, and measure from these grand averages, these measures do not differ across conditions
Making a grand average leads to the same problems as averaging across trials
  Greater latency variability across subjects in one group will lead to lower peak amplitude in this group’s grand average
  The onset time in the grand average will reflect the onset times of the subjects with the earliest onset times
Think about it, and make sure you get the same general pattern with conventional statistics
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 19: Jackknife Approach
Condition B
Sub1
Sub2
Sub3
Sub4
Sub1
Sub2
Sub3
Sub4
Stim
Stim
Mean of single-subject values
Mean of single-subject values
Condition A
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 20: Jackknife Approach
Condition A
Condition B
Sub1
Sub2
Sub3
Sub4
Sub1
Sub2
Sub3
Sub4
Stim
Stim
Mean of single-subject values
Mean of single-subject values
Value from grand average
Value from grand average
A difference in timing variability is misconstrued as a difference in mean onset time
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 21: Problem of Multiple Comparisons
If we do 10 independent statistical tests, and the null hypothesis is true for all 10, there is a 41% chance that at least one will be significant (false positive)
Example: Assessing side effects of Starbukine
Notes: Photo: https://commons.wikimedia.org/wiki/File:Guangzhou_Starbucks_01b.jpg (public domain)
All other material: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 22
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 23
Bonferroni Correction- 5% chance of even a single bogus p value in a family of tests (if the null is true for all tests)
If you find 100 significant values, there is only a 5% chance that even a single one of them will be bogus
False Discovery Rate (FDR) Correction- 5% of the significant tests would be expected to be bogus (if the null is true for all tests)
If you find 100 significant values, you would expect that ~5 would be false positives
If the null hypothesis is true for all tests, FDR = Bonferroni
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 24: Multiple Implicit Comparisons
In ERP research, we often have the “problem of multiple implicit comparisons”
  By eye, we compare two conditions at multiple time points and at multiple electrode sites
  Then we do our statistical analyses only for the time regions and electrode clusters where we see an effect
This can dramatically inflate the Type I error rate
  Even if the null hypothesis is true, you will almost always be able to find a “significant” difference in some time periods at some electrode sites
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 25: An Example
Take 640 standards per subject from a real oddball experiment
Divide them randomly into 512 “Standards” and 128 “Targets”
Null hypothesis is true by definition
Any differences are a result of sampling error
Goal: Simulate a null effect in an oddball experiment
Notes: Adapted from Figure 10.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 26: Simulated Standards & Targets
Broadly distributed across the right hemisphere
Limited to C3/C4/P3/P4
We know with 100% certainty that these effects are bogus because the simulated standards and targets were selected at random from a single population of trials
Notes: Adapted from Figure 10.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 27: Simulated Standards & Targets
“P1 effect”
  Measure mean amplitude from 50-150 ms at all electrodes
  Main effect of condition: p = .051
  Condition x hemisphere interaction: p = .011
“P2 effect”
  Measure mean amplitude from 150-250 ms at C3/C4/P3/P4
  Main effect of condition: p = .026
These effects are completely bogus and are significant only because we used the observed results to select the time periods and electrodes sites for the analysis
Broadly distributed across the right hemisphere
Limited to C3/C4/P3/P4
Notes: Adapted from Figure 10.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 28: Hints for Detecting Bogus Effects
Don’t believe effects that are implausibly early
  Effects prior to 100 ms are almost certainly bogus unless they are stimulus effects or spatial attention effects
Don’t believe effects at unexpected electrode sites
  P1 is not usually seen over front half of the head
Don’t believe effects that start near time zero and last a long time
Demand a replication before you believe
Apply these standards to your own data!
Broadly distributed across the right hemisphere
Limited to C3/C4/P3/P4
Notes: Adapted from Figure 10.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 29: Choosing Time Windows
Alternative 1: A priori window
Alternative 2: Average across conditions/groups to find appropriate window
  2a: Peak ± 100 ms (or 200, or 300, etc.)
  2b: In factorial design, look at difference wave for one factor collapsed across the other factor (e.g., rare-minus-frequent collapsed across patient/control)
Alternative 3: “Functional localizer” condition to find temporal “ROI”
  Example: Faces vs. Cars to find N170 window (and then use this window for a more subtle comparison, such as Males vs Females)
Alternative 4: Use large window with “signed area” and permutation test
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 30: Signed Area
Question: Is Rare–Frequent difference > 0?
Problem: Signed area is biased (always >= 0) — what value would we expect if Rare and Frequent are identical except for noise?
Solution: Use permutation approach to determine null distribution (negative area value expected if Rare = Frequent)
We can use a large a priori measurement window without suffering cancellation
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 31: The Permutation Approach
For published example, see
Sawaki, Geng, & Luck (2012, JNeurosci)
General logic: To determine the value expected by random chance, randomly shuffle the data to see what value is produced by chance
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 32: Choosing Time Windows
Alternative 5: Measure mean amplitude from multiple sequential time periods and use time as a factor in the ANOVA
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 33: Example: Consecutive Time windows for N2ac
Notes: Adapted with permission from Figure 1 from Gamble, M. L., & Luck, S. J. (2011). N2ac: An ERP component associated with the focusing of attention within an auditory scene. Psychophysiology, 48. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 34: Example: Consecutive Time windows for N2ac
Key Effects
Difference from zero: Significant
Time: Significant
Electrode: ns
Measure: Difference wave from 200-300, 300-400, 400-500, 500-600 ms at each electrode
Contra/Ipsi Test @ Each Time Interval
200-300: Significant
300-400: Significant
400-500: Significant
500-600: ns
Notes: Adapted with permission from Figure 1 from Gamble, M. L., & Luck, S. J. (2011). N2ac: An ERP component associated with the focusing of attention within an auditory scene. Psychophysiology, 48. This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 35: Choosing Time Windows
Alternative 1: A priori window
Alternative 2: Average across conditions/groups to find appropriate window
  2a: Peak ± 100 ms (or 200, or 300, etc.)
  2b: In factorial design, look at difference wave for one factor collapsed across the other factor (e.g., rare-minus-frequent collapsed across patient/control)
Alternative 3: “Functional localizer” condition to find temporal “ROI”
  Example: Faces vs. Cars to find N170 window (and then use this window for a more subtle comparison, such as Males vs Females)
Alternative 4: Use large window with “signed area”
Alternative 5: Use time as a factor in the ANOVA
Alternative 6: Mass univariate approach
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 36: Choosing Electrode Sites
Alternative 1: A priori region of interest
  May average across sites prior to measuring amplitude/latency
Alternative 2: All sites in an omnibus ANOVA
  May collapse into a smaller number of clusters first
  Usually involves looking for condition x electrode interaction (low power, especially with Greenhouse-Geisser correction)
Alternative 3: Use “functional localizer” condition
  Example: Faces vs. Cars to find N170 ROI (and then use this ROI for a more subtle comparison, such as Males vs Females)
Alternative 4: t test at each electrode with Bonferonni correction for multiple comparisons (very low power)
  Or false discovery rate correction (not quite as bad)
Alternative 5: Mass univariate approach
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 37: The Mass Univariate Approach
Goal: Avoid biases introduced by selecting time windows or electrode sites
General approach: Test all time points and all electrode sites, with an intelligent correction for multiple comparisons
  May have thousands of t values (# of time points x # of electrode sites)
  Several different approaches to correction are possible
Potential problem: low power
  Power can be increased if have a priori information that can reduce the number of time points or electrode sites
  For example, analyze 200-800 ms at posterior electrode sites
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 38: Example Experiment
12 subjects
300 time points (0-600 ms, 500 Hz)
10 electrode sites
3000 t tests
150 (5%) bogus effects expected without correction
Notes: Adapted from Figure 13.1 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 39: Rare Minus Frequent t Values
Notes: Adapted from Figure 13.2 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 40: Rare Minus Frequent t Values
Uncorrected
Notes: Adapted from Figure 13.2 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 41: Rare Minus Frequent t Values
Uncorrected
Bonferroni
Nothing is significant after correction except the very end of the P3 wave at C3, C4, and P3
However, we can be very confident that every single one of the significant points is real
Only 5% chance that even one of the significant effects is bogus
Notes: Adapted from Figure 13.2 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 42: Rare Minus Frequent t Values
Uncorrected
Bonferroni
False Discovery
Rate (B&Y) after downsampling to 125 Hz and limiting analysis period to 200-600 ms
Many more points are significant with FDR
We would expect that only 5% of the significant points are bogus
Notes: Adapted from Figure 13.2 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.

## Slide 43: Looking for Clusters
Uncorrected
Find all clusters of points that are significant at p < .05 uncorrected
Cluster is 2 or more adjacent time points or electrode sites
“Cluster mass” is the sum of the t values in a cluster
How big must a cluster mass be to be considered significant?
Cluster #1
Cluster #2
Notes: Adapted from Figure 13.5 in Luck, S.J. (2014). An Introduction to the Event-Related Potential Technique, Second Edition. Cambridge, MA: MIT Press. © MIT Press.
This material may be used for nonprofit research and education purposes only, and it may not be reprinted or distributed in any form including print and electronic forms.